## Slide 1: FPGA Neural Network
Alex Karantza & Sam Skalicky

## Slide 2: What are Neural Networks?
The history of computer science is filled with attempts to mimic biological systems
Neural networks are a kind of optimization function, modeled after a functional understanding of the cells that make up the animal nervous system

## Slide 3: What are Neural Networks?
Artificial Neural Networks are directed graphs
The nodes are Neurons, and the connections are Weights
In a feed-forward network, inputs are entered at one end and results are produced at the other
This kind of three-layer network is very common

## Slide 4: What are Neural Networks?
Neural Networks can learn
By adjusting the connection weights, the output neurons can describe any function
Even functions specified only incompletely, or by example
Training a network is the same as minimizing the function with respect to the weights

## Slide 5: How a Network Understands ⊕
F(x, y) ≃ x ⊕ y
A composition of nonlinear functions
With enough neurons, any dimensionality and complexity can be learned

## Slide 6: Goals for this project
Learn about FPGAs
Implement accurate algorithms
IEEE Floating Point
Implement a Fast Neural Network
4 bit text recognition
Scalable Network

## Slide 7: FPGA Implementation
We implemented a network capable of learning any two-input function, such as AND, OR, XOR, etc
This is the smallest network that is useful
It could be expanded to any size, simply by increasing the number of nodes

## Slide 8: Structural Overview
Neuron: sums up signals
Connection: passes along weighted signals
Sigmoid: clamps large unsigned values
Network: sets up topology, uses above
Interface/Testbench

## Slide 9: Dealing with Numbers
FPGA has no floating point support
Use fixed point signed & unsigned numbers, converting where necessary
Sigmoid requires a lot of dynamic range
Taylor series is best, we settled for a piecewise linear approximation

## Slide 10: The Sigmoid Function
Continuous
Piecewise

## Slide 11: User Interaction
Inputs
  Output type
  Function
  Input values
Output
  8 LEDs

## Slide 12: Live Demo

## Slide 13: Device Utilization & Performance
Node | Levels | Time
Data In | 29 | 13ns
Data Out | 2 | 5ns
Table 2: Data Speed |  | 
Total resources used: 19% | Device Utilization Summary |  | 
Logic Utilization | Used | Available | Utilization
Number of Slice Latches | 22 | 1,920 | 1%
Occupied Slices | 197 | 960 | 20%
4 input LUTs | 360 | 1,920 | 18%
 | Logic | 328 | 17%
 | Route-thru | 32 | 3%
Number of bonded IOBs | 10 | 108 | 9%
MULT18X18SIOs | 4 | 4 | 100%
Table 1: Device Utilization table for Spartan 3E-100 |  |  | 

## Slide 14: Conclusion
Demonstrated the feasibility of applying a theoretical understanding of neural networks to the design of a parallel asynchronous digital system
The prototype was limited by the computational resources available, but could be expanded with little effort
Biologically-inspired algorithms can be useful to solve difficult problems, and hardware can implement them effectively

## Slide 16: Diagram

## Slide 17: Diagram

## Slide 18: Diagram

## Slide 19: Diagram